TV BOX—X8 X9

USER MANUAL

WELCOME！

Thank you for purchasing this device。it brings you wonderful user experience. Before beginning, please refer to this user manual carefully. In case of any doubts regarding PIPO X8, you are welcomed to visit the PIPO official Facebook website: www.facebook.com/pipocn, for raising your questions and sharing your experience。Thank you！

Product features：

- WiFi connection，achieve displaying synchronization easily；

- Based on Intel Baytrail 3736F architecture，processor frequency is 2.16GHz；

# Chapter one A Glance on X8 X9

## 一、 X8 Appearance

KEYS

1：Power Switch key,

2 6： USB port, for connecting peripherals

3： Earphone jack

5: TF card slot: for TF card , maximum to 64GB

7: HDMI port

8: Lan RJ45 for internet cable

9: DC 12V power supply jack

## 二、Product Specifications

| Items | Function description |
| --- | --- |
| 1 | Processor | Baytrail 3736F ，frequency is 1.83GHz,up to 2.16 |
| 2 | LCD | 7”1280*800 |
| 3 | RAM | 2GB |
| 4 | Storage | 32GB OR 64GB |
| 5 | OS | Windows 8.1 with Bing + Android 4.4 |
| 4 | WiFi | 2.4GHz , WiFi signal； |
| 6 | Connection ports | HDMI 1.4； MicroUSB for power supply and upgrading, and USB2.0 for peripherals； |
| 7 | Switch key | Mode switching、reset 、upgrading key； |
| 8 | Bluetooth | 4.0 |

## 三、 X8 Accessories：

| Name |  | quantity |
| --- | --- | --- |
| Power charger | pc | 1 |
| User manual | pc | 1 |

# CHAPTER TWO  Operations

## 一、OS operation

1. Connect 12V 2.4A Charger to the X8 DC jack for power supplying；

2. press power button for a few seconds to turn it on;

3. Select Android or Windows, press Android icon to go to regular Android OS , and press Windows icon to go to Windows system

4.OS Switch

When you are in Windows system press the Win to And Icon for switching into Android

When you are in Android system, slide the top right corner, and press the OS switch icon to set up into Windows

5.HDMI output

Go to “Device”-“project”, and connect X8 to TV set (any display ) via HDMI cable

5.1 PC screen only

Images could be shown only in TV BOX X8, HDMI output will be cut off

5.2 Duplicate

The HDMI output on the TV set may be not by full screen, This is  because of the X8 LCD solution is 1280*800, so the HDMI output on the TV set is also shown by 1280*800

5.3 Extend

When you set up Project mode into Extend, then the X8 rotation may

Be locked, you can not rotate the X8 LCD. Press the desktop for a few seconds, go to the setting like this in the picture. ”graphics options ”—“rotation”—“built-in display” or “digital television”, to set up rotation here

The X8 LCD is the first screen, and the TV set display is the second screen, move the mouse pointer outside of first screen, it will jump into second screen and if you move the mouse pointer outside of screen screen, the mouse pointer will jump into first screen. First screen and second screen are separate displays, you can do different task on first screen and second screen. For example watching video on second screen, and the the same time skype chat or what’s app chat with friends on the first screen. There is a lot of fun in the Extend mode, just explore into it!

5.4 Second screen only

In this mode, the images could only be shown on the TV set display,

And the X8 LCD will be light off. And the second screen image may be upside down. Then please rotate the X8, place the X8 to be landscape mode or portrait mode, the second screen could be adjusted to normal displaying.

## Other functions

- Reset

# To reset or recover the X8, go to “setting”--”change PC setting”—“update and recovery”

- System upgrading and software fixing

Please download the WINPE-TOOLS and X8 Images from PIPO official website: www.pipo.cn/en  service section

# Procedure：

# 1 copy the WINPE_TOOLS file to the USB storage, place this file to the ROOT(USB format to be NTFS and FAT32, it depends on Images, for example W3, the install .wim file is bigger than 4GB in size, the format to be NTFS), the USB name shall be : WINPE

# 2. Copy the Images into "Image" of WIMPE_TOOLS, for example, copy the " install.wim "  & " winre.wim " in W3 folder into the images folder of WINPE_TOOLS

# If install W4, enter into script, change the main_w4.cmd into Main.cmd, delete another main.cmd or rename it

# after all of the above steps, start the tablets with the USB storage inserted.

## Declaration

Poisonous substances as shown bellow：

| parts | Dangerous substance |
| --- | --- |
|  | （Pb） | （Hg） | （Cd） | （Cr6+） | （PBB） | （PBDE） |
| Case | ○ | ○ | ○ | × | × | ○ |
| PCB | × | ○ | ○ | ○ | × | × |
| Battery | × | ○ | ○ | × | ○ | ○ |
| LCD | ○ | ○ | ○ | ○ | ○ | ○ |
| Cable | × | ○ | ○ | ○ | × | × |

○：

×：