TV BOX—X10

USER MANUAL

WELCOME！

Thank you for purchasing this device。it brings you wonderful user experience. Before beginning, please refer to this user manual carefully. In case of any doubts regarding PIPO X10, you are welcomed to visit the PIPO official Facebook website: www.facebook.com/pipocn, for raising your questions and sharing your experience。Thank you！

Product features：

- WiFi connection，achieve displaying synchronization easily；

- Based on Intel 8300 architecture，processor frequency is 1.84GHz；

# Chapter one A Glance on X10

## 一、 X10 Appearance

KEYS  from left to Right

1：Power Switch key,

2 6： USB port, for connecting peripherals

3： Earphone jack

5: TF card slot: for TF card , maximum to 64GB

7: HDMI port

8: Lan RJ45 for internet cable

9: DC 5V power supply jack

10:  RS232 port, optional

## 二、Product Specifications

| Items | Function description |
| --- | --- |
| 1 | Processor | Intel Cherrytrail 8300, Quad-core, up to 1.84GHz |
| 2 | LCD | 10.8’’ 1920*1280 |
| 3 | RAM | 4GB DDR 3L |
| 4 | Storage | 64GB |
| 5 | OS | Windows 10 home, Office(Word mobile, PPT mobile, Excel mobile ) |
| 4 | WiFi | 802.11 b/g/n |
| 6 | Connection ports | USB(to device) *4, HDMI output, Micro SD slot，Audio output, RJ45, cooling fan |
| 7 | Switch key | Mode switching、reset 、upgrading key； |
| 8 | Bluetooth | 4.0 |

## 三、 X10 Accessories：

| Name |  | quantity |
| --- | --- | --- |
| Power charger | pc | 1 |
| User manual | pc | 1 |

# CHAPTER TWO  Operations

## 一、OS operation

1. Connect 5V 3A Charger to the X10 DC jack for power supplying；

2. press power button for a few seconds to turn it on;

3.HDMI output

Go to “Device”-“project”, and connect X10 to TV set (any display ) via HDMI cable

5.1 PC screen only

Images could be shown only in TV BOX X10, HDMI output will be cut off

5.2 Duplicate

Whatever shown on the X10  will be cast to other displays via HDMI cable

5.3 Extend

When you set up Project mode into Extend, then the X10 rotation may

Be locked, you can not rotate the X10 LCD. Press the desktop for a few seconds, go to the setting like this in the picture. ”graphics options ”—“rotation”—“built-in display” or “digital television”, to set up rotation here

The X10 LCD is the first screen, and the TV set display is the second screen, move the mouse pointer outside of first screen, it will jump into second screen and if you move the mouse pointer outside of screen screen, the mouse pointer will jump into first screen. First screen and second screen are separate displays, you can do different task on first screen and second screen. For example watching video on second screen, and the the same time skype chat or what’s app chat with friends on the first screen. There is a lot of fun in the Extend mode, just explore into it!

5.4 Second screen only

In this mode, the images could only be shown on the TV set display,

And the X10 LCD will be light off. And the second screen image may be upside down. Then please rotate the X10, place the X10 to be landscape mode or portrait mode, the second screen could be adjusted to normal displaying.

## Other functions

- Reset

# To reset or recover the X10, go to “setting”--”change PC setting”—“update and recovery”

- System upgrading and software fixing

Please download the WINPE-TOOLS and X8 Images from PIPO official website: www.pipo.cn/en  service section

# Procedure：

# 1 copy the WINPE_TOOLS file to the USB storage, place this file to the ROOT(USB format to be NTFS and FAT32, it depends on Images, for example W3, the install .wim file is bigger than 4GB in size, the format to be NTFS), the USB name shall be : WINPE

# 2. Copy the Images into "Image" of WIMPE_TOOLS, for example, copy the " install.wim "  & " winre.wim " in W3 folder into the images folder of WINPE_TOOLS

# If install W4, enter into script, change the main_w4.cmd into Main.cmd, delete another main.cmd or rename it

# after all of the above steps, start the tablets with the USB storage inserted.

## Declaration

Poisonous substances as shown bellow：

| parts | Dangerous substance |
| --- | --- |
|  | （Pb） | （Hg） | （Cd） | （Cr6+） | （PBB） | （PBDE） |
| Case | ○ | ○ | ○ | × | × | ○ |
| PCB | × | ○ | ○ | ○ | × | × |
| Battery | × | ○ | ○ | × | ○ | ○ |
| LCD | ○ | ○ | ○ | ○ | ○ | ○ |
| Cable | × | ○ | ○ | ○ | × | × |

○：

×：